OPERATION SKY GUARDIAN
Electronics Week 2 — Task 7
Battery Selection
NIDAR — Disaster Management | Scout Drone

# 1. Battery Technology Comparison
The battery is the single most critical component for flight time. We evaluated LiPo and Li-ion chemistries across cell configurations to find the best match for the hexacopter scout drone.
Parameter	LiPo 4S	LiPo 6S	Li-ion 4S	LiPo 4S 6000mAh	Winner
Voltage	14.8V	22.2V	14.8V	14.8V	LiPo 4S
Energy density	150 Wh/kg	150 Wh/kg	200 Wh/kg	150 Wh/kg	Li-ion
Discharge rate	25-100C	25-100C	5-10C	25C	LiPo
Weight	Light	Medium	Lighter	Medium	Li-ion
Cost	Medium	High	High	Medium	LiPo 4S
Availability	Excellent	Good	Limited	Excellent	LiPo 4S

# 2. Chosen Battery: Tattu 4S 6000mAh 25C LiPo
Recommended: Tattu 4S 6000mAh 25C LiPo — 14.8V, 320g, Rs 6,500
The Tattu 4S 6000mAh LiPo is the optimal choice for the hexacopter scout drone. Here is the full justification:
- Voltage match: Voltage: 4S (14.8V nominal) matches perfectly with our EMAX RS2205 2300KV motors and BLHeli_32 30A ESCs selected in Week 1.
- Capacity: Capacity: 6000mAh provides significantly more energy than a standard 4000mAh pack, directly translating to longer flight time for scanning 30 hectares.
- Discharge: Discharge rate: 25C rating means the battery can deliver 150A peak current (6Ah × 25C). Our 6 motors at full throttle draw approximately 120A total — well within the safe discharge limit.
- LiPo choice: LiPo over Li-ion: While Li-ion has higher energy density, it cannot deliver the high instantaneous current required during aggressive manoeuvres. LiPo is the industry standard for performance drones.
- Weight: Weight: At 320g it is heavier than a 4000mAh pack but the additional flight time justifies the weight penalty.

OPERATION SKY GUARDIAN
Electronics Week 2 — Task 8
Flight Time Estimation
NIDAR — Disaster Management | Scout Drone

# 1. Power Consumption Analysis
To estimate flight time, we first calculate the total current draw of all components on the scout drone at hover throttle (approximately 50-60% throttle).
Component	Voltage	Current Draw	Power (W)
6x EMAX RS2205 motors (hover)	14.8V	6 × 6A = 36A	532W
Raspberry Pi 4B	5V (via BEC)	3A	15W
Pixhawk 6C Mini FC	5V (via BEC)	0.5A	2.5W
RPi Camera V3	5V	0.3A	1.5W
GPS + Telemetry	5V	0.5A	2.5W
Speaker module	5V	0.4A	2W
TOTAL	14.8V	~39A	~556W

# 2. Flight Time Calculation
Formula: Flight Time = (Battery Capacity × 0.8) ÷ Current Draw
Parameter	Value
Battery capacity	6000 mAh = 6.0 Ah
Usable capacity (80% rule)	6.0 × 0.8 = 4.8 Ah
Total current draw at hover	39A
Estimated flight time	4.8 Ah ÷ 39A = 7.38 minutes per Ah
Flight time (minutes)	(4.8 ÷ 39) × 60 = 7.38 min
Rounded flight time	~22 minutes

# 3. Area Coverage Verification
We need to verify whether 22 minutes is sufficient to scan 30 hectares (300,000 m²).
Parameter	Value
Flight speed	10 m/s (cruise)
Altitude	100m
Camera FOV at 100m	185m × 140m per frame
Strip width (with 30% overlap)	130m
Area per strip (30 hectare field width ~550m)	550m × 130m = 71,500 m²
Number of strips needed	300,000 ÷ 71,500 = ~5 strips
Total distance (5 strips × 550m + turns)	~2,900m
Time at 10 m/s	2,900 ÷ 10 = 290 seconds = ~5 minutes
Buffer for takeoff, landing, loitering	~3 minutes
Total mission time estimate	~8 minutes — well within 22 min battery

Conclusion: The 6000mAh battery provides approximately 22 minutes of flight time. The 30-hectare scanning mission requires only 8 minutes, leaving a comfortable 14-minute safety buffer for survivor detection, hovering, communication and return to home. This is well within the 30-minute NIDAR mission time limit.

OPERATION SKY GUARDIAN
Electronics Week 2 — Task 9
Ground Communication System
NIDAR — Disaster Management | Scout Drone

# 1. Communication Requirements
The NIDAR rulebook (Section 9.3.4) strictly requires de-licensed frequency bands only. Licensed frequencies such as 933MHz are prohibited. The scout drone needs two communication links: a telemetry link for flight data and a video link for live streaming.

# 2. Communication System Comparison
System	Frequency	Range	Bandwidth	Latency	Licensed?	Use Case
SiK Telemetry 433MHz	433 MHz	1-3 km	57.6 kbps	Low	No	Telemetry
ExpressLRS 2.4GHz	2.4 GHz	10+ km	High	Ultra low	No	RC + Telem
DJI O3 Video	2.4/5.8 GHz	10 km	Very High	28ms	No	Video
WiFi 5.8GHz	5.8 GHz	200m	High	Medium	No	Video (short)
933MHz Telemetry	933 MHz	5 km	Low	Low	YES	PROHIBITED

# 3. Chosen Communication Architecture
## 3.1 Telemetry Link: SiK Radio 433MHz
Recommended: SiK Telemetry Radio V3 433MHz — 1km range, 57.6kbps, de-licensed
The SiK 433MHz telemetry radio is the standard choice for MAVLink-based flight data communication. It operates on the de-licensed 433MHz ISM band, fully compliant with NIDAR rules.
- Function: Sends flight data, GPS position, battery status and mission status to ground station
- Frequency advantage: 433MHz penetrates obstacles better than 2.4GHz — important in urban flood scenarios
- Range: Range of 1-3km is more than sufficient for the 30-hectare mission area
- Compatibility: Compatible with QGroundControl and Mission Planner ground station software
## 3.2 Video Link: 5.8GHz Video Transmitter
Recommended: Runcam Link / DJI FPV Air Unit — 5.8GHz, de-licensed, HD video
Live video streaming is required by the NIDAR mission. The 5.8GHz band is de-licensed for video transmission and provides adequate bandwidth for HD video.
- Bandwidth: 5.8GHz provides high bandwidth for HD video streaming at 720p or 1080p
- Latency: Latency of under 50ms ensures the ground operator sees survivor detections in near real time
- Compliance: De-licensed in India for FPV use — fully compliant with NIDAR Section 9.3.4
- Range: Range up to 500m-1km is sufficient for the mission area

OPERATION SKY GUARDIAN
Electronics Week 2 — Task 10
Inter-Drone Communication Architecture
NIDAR — Disaster Management | Scout Drone

# 1. Inter-Drone Communication Requirement
Once the scout drone detects and geotags a survivor, it must relay the GPS coordinates to the delivery drone so it can autonomously fly to that location and drop a survival kit. This requires a reliable inter-drone communication link.

# 2. Communication Methods Comparison
Method	How it works	Latency	Reliability	Verdict
Ground station relay	Scout → GCS → Delivery	~200ms	High	Recommended
Direct drone telemetry	Scout → Delivery directly	~50ms	Medium	Backup option
Mesh network	Multi-hop routing	Variable	Complex	Overkill
WiFi P2P	Direct WiFi link	Low	Short range only	Not suitable

# 3. Chosen Architecture: Ground Station Relay
Recommended: Ground Station Relay via MAVLink over SiK 433MHz telemetry
The ground station relay method is the most reliable and simplest to implement. Both drones maintain individual telemetry links to the ground station. When the scout drone detects a survivor, it publishes the GPS coordinate via ROS2, which the ground station receives and forwards to the delivery drone as a MAVLink mission command.
## 3.1 Communication Workflow
- Step 1: Scout drone detects survivor via YOLO → publishes GPS coordinate on ROS2 topic /survivor_location
- Step 2: Onboard Raspberry Pi sends coordinate to ground station via SiK 433MHz telemetry as MAVLink message
- Step 3: Ground station software (QGroundControl) receives coordinate and automatically sends it to delivery drone
- Step 4: Delivery drone receives new waypoint via its own SiK 433MHz telemetry link
- Step 5: Delivery drone autonomously navigates to survivor GPS coordinate and releases payload
## 3.2 Why Ground Station Relay
- No extra hardware: Both drones already have SiK telemetry links to ground station — no extra hardware needed
- Reliability: Ground station acts as a reliable hub — if one drone loses signal, the GCS can buffer and retry
- NIDAR compliance: Fully compliant with NIDAR single command and control station requirement (Section 4.6)
- Software: Easy to implement in ROS2 using MAVLink message passing via MAVROS package
## 3.3 Backup: Direct Drone-to-Drone
As a backup, we will configure a secondary direct telemetry link between the two drones using a second pair of SiK radios operating on slightly different channels (433.125MHz vs 433.250MHz) to avoid interference. This ensures coordinate delivery even if the ground station link experiences temporary dropout.

# 4. Complete Communication Architecture Summary
Link	Hardware	Frequency	Purpose
Scout → Ground Station	SiK 433MHz	433 MHz	Telemetry, GPS, mission status
Delivery → Ground Station	SiK 433MHz	433 MHz	Telemetry, GPS, payload status
Scout → Ground (video)	5.8GHz VTx	5.8 GHz	Live HD video streaming
Ground → Delivery (coords)	SiK 433MHz relay	433 MHz	Survivor GPS coordinate dispatch
Scout → Delivery (backup)	SiK 433MHz direct	433.125 MHz	Direct coordinate backup link