OPERATION SKY GUARDIAN
Electronics Week 1 — Task 4
Camera Selection for Area Scanning
NIDAR Disaster Management | Scout Drone | March 2026

# 1. Mission Requirement
The scout drone must scan 30 hectares of flooded terrain and stream real-time video to the ground station. The camera needs to be lightweight, have a wide field of view, support streaming, and provide enough resolution to clearly identify a human survivor on a rooftop from an altitude of 80 to 120 metres.

# 2. Camera Comparison Table
Camera	Resolution	FOV	Frame Rate	Weight	Interface	Streaming
Raspberry Pi Camera V3	12 MP	102°	30 fps	4 g	CSI	Via RPi, low latency
Sony IMX477 (HQ Cam)	12.3 MP	63–120°	30 fps	30 g	CSI	Via SBC
GoPro Hero 12	27 MP	156°	60 fps	153 g	USB/HDMI	Via WiFi
RunCam Phoenix 2	1.8 MP	155°	60 fps	15 g	Analog	FPV only
OpenMV Cam H7	3.2 MP	70°	30 fps	8 g	SPI/USB	Limited

# 3. Chosen Camera: Raspberry Pi Camera V3
Recommended choice: Raspberry Pi Camera Module V3 — 12MP, 102° FOV, 4g
The Raspberry Pi Camera V3 is the ideal choice for this mission. Here is why:
- Resolution: Resolution: 12 megapixels gives enough detail to identify a human from 100m altitude. The image covers roughly 150m × 110m per frame at that height.
- Field of view: FOV: The 102° wide angle field of view maximises ground coverage per pass, reducing the number of passes needed to scan 30 hectares.
- Weight: Weight: At just 4 grams, it adds negligible weight to the scout drone, preserving battery life and flight time.
- Integration: Integration: Directly connects to the Raspberry Pi via CSI ribbon cable — no additional adapters needed. Python libraries like Picamera2 make streaming straightforward.
- Streaming: Streaming: Live H.264 video can be streamed to the ground station over WiFi or a dedicated video link at under 100ms latency.
- Cost: Cost: Approximately Rs 4,000 — affordable and easily replaceable.

# 4. Area Scanning Strategy
At 100m altitude with a 102° FOV, each camera frame covers approximately 185m × 140m of ground. To scan 30 hectares (300m × 1000m equivalent area), the scout drone will fly a lawnmower grid pattern with 80m strip spacing to ensure 30% overlap between passes for complete coverage.
- Estimated passes needed: 4 to 5 parallel strips
- Strip width: 140m (with overlap)
- Total scan time at 10 m/s: approximately 18 to 22 minutes
- This fits comfortably within the 30-minute NIDAR mission time limit

OPERATION SKY GUARDIAN
Electronics Week 1 — Task 5
Motor and ESC Research
NIDAR Disaster Management | Scout Drone | March 2026

# 1. Motor Selection
The scout drone motors need to provide enough thrust to lift the entire system while being efficient enough to achieve 20+ minutes of flight time. We evaluated motors based on KV rating, thrust, current draw and efficiency.
## 1.1 Motor Comparison Table
Motor	KV Rating	Max Thrust	Current (hover)	Weight	Verdict
EMAX RS2205 2300KV	2300 KV	780g	6A	28g	Recommended — efficient, light
T-Motor F40 Pro 2400KV	2400 KV	850g	7A	30g	Good but slightly heavy current
Sunnysky X2212 980KV	980 KV	650g	4.5A	52g	Too heavy for scout role
DJI 2312E 960KV	960 KV	800g	5A	56g	Good thrust, too heavy

## 1.2 Chosen Motor: EMAX RS2205 2300KV
Recommended choice: EMAX RS2205 2300KV — 780g thrust, 28g weight, 6A hover current
The EMAX RS2205 2300KV offers the best balance of thrust, efficiency and weight for the scout drone role. At hover, each motor draws approximately 6A, giving a total of 24A for all four motors. This fits well within our battery and ESC specifications.
- Thrust ratio: Thrust to weight: Each motor produces 780g thrust. Total thrust = 3120g. Scout drone target takeoff weight = 1400g. Thrust ratio = 2.2:1 — excellent for stable flight.
- KV rating: The 2300KV rating pairs well with 5-inch propellers on a 4S battery for efficient cruising flight.
- Weight: At just 28g each, all four motors add only 112g to the frame — critical for maximising endurance.

# 2. ESC Selection
ESCs (Electronic Speed Controllers) convert the flight controller's PWM signals into three-phase power for the brushless motors. They must handle the motor's peak current with a safety margin.
## 2.1 ESC Comparison Table
ESC	Current Rating	Voltage	Protocol	Weight	Verdict
BLHeli_32 30A	30A cont.	3-6S	DSHOT600	9g	Recommended — reliable, light
KISS 24A Race Edition	24A cont.	3-5S	DSHOT300	5g	Good but tight current margin
Hobbywing XRotor 40A	40A cont.	3-6S	PWM/DSHOT	22g	Overkill — too heavy
Favourite FVT 20A	20A cont.	2-4S	PWM	8g	Insufficient current rating

## 2.2 Chosen ESC: BLHeli_32 30A
Recommended choice: BLHeli_32 30A ESC — DSHOT600, 3-6S, 9g weight
The BLHeli_32 30A ESC is chosen for its compatibility with the EMAX RS2205 motor and the flight controller's DSHOT600 digital protocol. The 30A rating gives a healthy safety margin above the motor's 20A peak draw.
- Current safety: Current margin: Motor peak = 20A, ESC rating = 30A. Safety margin = 50% — ensures ESCs never overheat.
- Protocol: DSHOT600 protocol gives precise, noise-free throttle control compared to analogue PWM signals.
- Firmware: BLHeli_32 firmware supports bidirectional DSHOT for RPM telemetry, useful for flight controller tuning.
- Weight: At 9g each, four ESCs add only 36g total — very lightweight.

OPERATION SKY GUARDIAN
Electronics Week 1 — Task 6
Propeller and Core Electronics Selection
NIDAR Disaster Management | Scout Drone | March 2026

# 1. Propeller Selection
Propellers convert motor rotation into thrust. The right propeller must match the motor KV rating and battery voltage to maximise efficiency and flight time.
## 1.1 Propeller Comparison Table
Propeller	Diameter	Pitch	Thrust	Material	Verdict
HQProp 5x4.3x3	5 inch	4.3 inch	750g/motor	PC plastic	Recommended — efficient, durable
Gemfan 5152	5.1 inch	5.2 inch	820g/motor	PC plastic	Good thrust, higher current draw
DAL 5045	5 inch	4.5 inch	680g/motor	PC plastic	Good but slightly less efficient
Carbon fibre 6045	6 inch	4.5 inch	950g/motor	Carbon fibre	Too large for 450mm frame

## 1.2 Chosen Propeller: HQProp 5x4.3x3
Recommended choice: HQProp 5x4.3x3 tri-blade — 750g thrust, polycarbonate, 5 inch
The HQProp 5x4.3x3 is a tri-blade propeller that provides an excellent balance of thrust and efficiency. It pairs perfectly with the EMAX RS2205 2300KV motor on a 4S battery.
- Diameter: Diameter: 5 inches fits within the 450mm frame with adequate propeller clearance of at least 10mm on each side.
- Tri-blade: Tri-blade configuration provides smoother airflow and lower vibration compared to bi-blade, improving camera stability.
- Material: Polycarbonate material is durable, lightweight and resistant to minor crashes during testing.
- Thrust: At 4S voltage, each propeller produces approximately 750g of thrust — matching our motor selection perfectly.

# 2. Core Electronics Components
Beyond motors, ESCs and propellers, the scout drone requires several additional electronic components for flight control, navigation, processing and communication.
Component	Chosen Model	Key Specs	Justification
Flight Controller	Pixhawk 6C Mini	F7 CPU, 6-axis IMU, Barometer	Industry standard, ROS2 compatible, supports PX4 autopilot used in our simulation
GPS Module	Here3+ GNSS	Multi-constellation, RTK ready, compass	Essential for accurate geotagging of survivors. Multi-constellation gives reliable lock even in urban canyons
Telemetry Radio	SiK Telemetry 433MHz	1km range, 57.6kbps, 433MHz	De-licensed frequency band as required by NIDAR rulebook Section 9.3.4. Connects drone to ground station
Onboard Computer	Raspberry Pi 4B (4GB)	Quad-core 1.8GHz, 4GB RAM	Runs YOLO detection, ROS2 nodes, camera streaming and coordinate publishing simultaneously
Power Distribution	Matek HUBOSD 5-in-1	6S capable, 5V/12V BEC, OSD	Distributes battery power to all ESCs and provides regulated 5V to flight controller and RPi
Speaker Module	DFPlayer Mini + 2W speaker	MP3 playback, 3.7-5V	Fulfils NIDAR requirement to communicate with survivors via audio alert from the drone

# 3. Complete Scout Drone Component Summary
Component	Model	Weight	Cost (approx)
Frame	Custom X450 CF	350g	Rs 2,500
Motors (x4)	EMAX RS2205 2300KV	112g	Rs 6,000
ESCs (x4)	BLHeli_32 30A	36g	Rs 3,200
Propellers (x4)	HQProp 5x4.3x3	20g	Rs 800
Flight Controller	Pixhawk 6C Mini	38g	Rs 18,000
GPS Module	Here3+ GNSS	48g	Rs 12,000
Onboard Computer	Raspberry Pi 4B	46g	Rs 5,500
Camera	RPi Camera V3	4g	Rs 4,000
Telemetry Radio	SiK 433MHz	25g	Rs 2,500
Power Distribution	Matek HUBOSD	18g	Rs 1,800
Speaker Module	DFPlayer + speaker	15g	Rs 500
Battery (4S 4000mAh)	Tattu 4S 4000mAh	320g	Rs 6,000
TOTAL		~1032g	~Rs 62,800

Total estimated takeoff weight of approximately 1032g is well within the NIDAR maximum of 25kg. The thrust-to-weight ratio of 3:1 ensures stable autonomous flight and reliable hovering for survivor detection.